## Slide 1: OPEN AN UC
Security Level:

## Slide 2
OPEN AN-based electricity price collaboration for energy saving solution---For MTN Power Band Energy Saving
MAE
A2A-T
OSS
OSS Agents&Apps
Scenario-based energy saving UC
A2A-T intent translation
Translate energy-saving intentions
(Region, energy-saving target, safeguard target)
‌Integration of electricity price synergy and energy-saving intentions
Obtain and parse dynamic electricity pricing
Converting intents of Electricity price synergy and energy conservation
into A2A-T interface information
Energy saving and experience assurance intents
Time period | Energy saving and experience assurance intents | 
23~5 | Maximized energy saving | No rate guarantee target.
6~9 | Proactive energy saving | 10Mbps
10~15 | Experience first | No degrade
16~17 | Proactive energy saving | 10Mbps
18~22 | Experience first | No degrade
RAN
Intent
Data：CM、PM、MR/CHR
Monthly charging Band prediction
Site classification
Marking downgrade sites
Marking Upgrade sites
Marking Grade stable-maintained sites
Monthly collaborative optimization of electricity cost reduction at the cluster level
Cluster planning
for Electricity price synergy and energy conservation
Monthly power consumption prediction for per site
Monthly charging Band prediction for per site
Traffic migration-out for Downgrade / Upgrage sites by decreasing Power or increasing Tilt or HO out users
Coverage
&experience &energy consumption simulation
Cluster-level electricity cost minimization optimization
Traffic migration-in for Grade stable-maintained sites by decreasing Power or increasing Tilt or HO in users
electricity cost prediction
Band no. | Band | Total GHS
1 | 0.00-0.99KW | 8247.66
2 | 1.00-1.99KW | 10628.25
3 | 2.00-2.99KW | 11956.25
4 | 3.00-3.99KW | 15409.75
5 | 4.00-4.99KW | 17784.09

## Slide 3
OPEN AN-based Lithium Battery Charge and Discharge Planning Based on Electricity Prices
MAE
A2A-T
OSS
OSS Agents&Apps
Scenario-based energy saving UC
A2A-T intent translation
Translate energy-saving intentions
(Region, energy-saving target, safeguard target)
‌Integration of electricity price synergy and energy-saving intentions
Obtain and parse dynamic electricity pricing
Converting intents of Electricity price synergy and energy conservation
into A2A-T interface information
Energy saving and experience assurance intents
Time period | Energy saving and experience assurance intents | 
23~5 | Maximized energy saving | No rate guarantee target.
6~9 | Proactive energy saving | 10Mbps
10~15 | Experience first | No degrade
16~17 | Proactive energy saving | 10Mbps
18~22 | Experience first | No degrade
RAN
Intent
Data：CM、PM、MR/CHR
Planning the lithium battery charge and discharge periods based on electricity prices
Staggering Electricity Usage
Staggering Electricity Usage MML Generation and Delivery
Peroid | Price
0~5 | 1
6~9 | 1.176
10~15 | 0.824
16~17 | 1.176
18~21 | 1.765
22~23 | 1.176